## Slide 1: BROWNE’S ADDITION HISTORIC DISTRICT
Preliminary Approval of Nomination, Resource Pages & Design Standards

## Slide 2: Browne’s Addition Historic District

## Slide 3: Browne’s Addition Historic District

## Slide 4: Browne’s Addition Historic District 1st Avenue

## Slide 5: Browne’s Addition Historic District 1st Avenue

## Slide 6: Browne’s Addition Historic District 1st Avenue

## Slide 7: Browne’s Addition Historic District Riverside Avenue

## Slide 8: Browne’s Addition Historic District Riverside Avenue

## Slide 9: Browne’s Addition Historic District Riverside Avenue

## Slide 10: Browne’s Addition Historic District Pacific Avenue

## Slide 11: Browne’s Addition Historic District Pacific Avenue

## Slide 12: Browne’s Addition Historic District 2nd Avenue

## Slide 13: Browne’s Addition Historic District 2nd Avenue

## Slide 14: Browne’s Addition Historic District 3rd Avenue

## Slide 15: Browne’s Addition Historic District 3rd Avenue

## Slide 16: Browne’s Addition Historic District 4th Avenue

## Slide 17: Browne’s Addition Historic District 4th Avenue

## Slide 18: Browne’s Addition Historic District 5th Avenue

## Slide 19: Browne’s Addition Historic District 5th Avenue

## Slide 20: Browne’s Addition Historic District Sunset Boulevard

## Slide 21: Browne’s Addition Historic District Oak Street

## Slide 22: Browne’s Addition Historic District Elm Street

## Slide 23: Browne’s Addition Historic District Cannon Street

## Slide 24: Browne’s Addition Historic District Cannon Street

## Slide 25: Browne’s Addition Historic District Coeur d’Alene Park

## Slide 26: Browne’s Addition Historic District Chestnut Street

## Slide 27: Browne’s Addition Historic District Chestnut Street

## Slide 28: Browne’s Addition Historic District Hemlock Street

## Slide 29: Browne’s Addition Historic District Hemlock Street

## Slide 30: Browne’s Addition Historic District Spruce Street

## Slide 31: Browne’s Addition Historic District Poplar Street

## Slide 32: Browne’s Addition Historic District Coeur d’Alene Street

## Slide 33: Browne’s Addition Historic District Coeur d’Alene Street

## Slide 34: Browne’s Addition Historic District Modifications/Integrity
INTACT
The Queen Anne house was designed by Loren L. Rand in 1899 as a single-family residence, and was
converted to multi-family use in 1954. No visible modifications have occurred to the exterior of the house;
it retains excellent historic integrity and contributes to the Browne’s Addition Historic District.

## Slide 35: Browne’s Addition Historic District Modifications/Integrity
SLIGHT
Changes to plan are not entirely visible from the street and in-kind window replacement = slight

## Slide 36: Browne’s Addition Historic District Modifications/Integrity
MODERATE
The exterior is clad with stucco that appears
to have been added over other siding due to the shallow relief of the window frames. The windows on the
north façade are original wood fixed sash, and the windows on the west elevation have been replaced with
anodized aluminum sliding sash. Even so, the cottage has an intact porch and plan, and overall retains
good historic integrity.

## Slide 37: Browne’s Addition Historic District Modifications/Integrity
EXTENSIVE
The first and second stories are clad with stucco applied over the original siding,
and the third story is clad with wood shingle siding on the north façade. The windows have been replaced
with vinyl hung and sliding sash. Plan has been extensively changed with front porch enclosure and second story addition at rear.

## Slide 38: Browne’s Addition Historic District Levels of Integrity
EXCELLENT
No visible modifications have occurred to the exterior of the Colonial Revival house since it was
constructed in 1896; it retains excellent historic integrity and contributes to the Browne’s Addition Historic
District.

## Slide 39: Browne’s Addition Historic District Modifications/Integrity
GOOD
The Stick style house was constructed in 1889. Modifications to a small number of
windows only slightly reduce its historic appearance and integrity of design and materials. Overall, the
house retains good historic integrity, and contributes to the Browne’s Addition Historic District.

## Slide 40: Browne’s Addition Historic District Modifications/Integrity
FAIR
Constructed circa 1890, as depicted on the 1890 Sanborn Fire Insurance Map, as one of the earlier multifamily
residences in Browne’s Addition, replacement siding and windows reduce its historic appearance
and integrity of design and materials. Even so, with the intact plan and lively Queen Anne massing of
projecting bays and intact entrances, the apartment building retains enough historic integrity to still
contribute to the Browne’s Addition Historic District.

## Slide 41: Browne’s Addition Historic District Modifications/Integrity
POOR
Constructed in 1889, modifications to the plan, siding, and windows of the cottage have removed all evidence of its historic appearance and completely diminish its integrity of design, materials, workmanship, and association. The house does not retain historic integrity and does not contribute to the Browne’s Addition
Historic District.

## Slide 42: Browne’s Addition Historic District Modifications/Integrity
Changes over time
The Queen Anne house was designed by Cutter and Malmgren in 1898 as a single-family residence, and it was converted to a multi-family residence in 1925. Modifications to the plan with the partial enclosure of the porch in 1948 and presence of replacement siding and changes to windows somewhat reduce its historic appearance and integrity of design and materials. Even so, with the plan and massing otherwise intact, the dwelling retains good historic integrity and contributes to the Browne’s Addition Historic District.

## Slide 43: Browne’s Addition Historic District Contributing/Non-contributing

## Slide 44: Browne’s Addition Historic District Design Standards
historicspokane.org/pro-brownes

## Slide 45: Browne’s Addition Historic District
Actions concluded:
SHLC gave a preliminary approval to three documents:
  Browne’s Addition Spokane Register District Nomination
  Resource forms for Browne’s – gives determination of contributing and non-contributing
  Design Standards document
When will the final action be taken?
We are planning to have SHLC final meeting on the district at our June 19th meeting
Then City Council will approve district through the overlay zone ordinance

## Slide 46: Browne’s Addition Historic District
Property owner vote
Ballots mailed out mid-April to all property owners
We will have 60-days for the ballots to be returned
Major changes may be made to the documents before ballots mailed, small changes may continue to be made until final action by SHLC

## Slide 47: Browne’s Addition Historic District
What is next?
Logan is developing the overlay zone ordinance for Plan Commission and City Council
Instead of a Management Agreement, the overlay ordinance will be the action that City Council takes after the recommendation is given from the SHLC
Other HPO Duties:
We are developing a notice sign for the district and zoning ordinance
We will have to do a non-project SEPA for the district
The ordinance will have to go to the State Department of Commerce
It has to be reviewed by Plan Commission (first workshop April 24th) we will follow up soon after for a final recommendation from them to City Council
We will workshop it to City Council at an Urban Advantage Committee meeting – first in May

## Slide 48: Browne’s Addition Historic District
What can you do?
VOTE! Please return your ballots promptly after receiving them.
Encourage neighbors to vote as well!
Are you a tenant? Encourage your landlord to vote.
Email HPO with comments on the documents – big items before ballots are mailed, small changes can be made up until June.
Attend Plan Commission and City Council meetings when the Historic District Overlay Zone ordinance is up for discussion or vote.

## Slide 49: Questions…
General:
1. What surprised you about the documents?
2. What questions do you have about the documents?
3. Was there something missing from the documents that you expected to see?
4. Is there anything in the documents that you would like to see changed?

## Slide 50: Questions…
Nomination:
Did the nomination do a good job capturing the history, culture, and built environment that make Browne’s Addition worth protecting? If not, what was missing?
Do you feel the boundary accurately reflects the district? If not, what would you change?

## Slide 51: Questions…
Design Review Standards:
Were the Design Review Standards confusing? If so, which part could be clearer?
Do you want paint colors to be included in the design review process?
Do you want landscaping to be included in the design review process? What about garages?

## Slide 52: Questions…
Resource Forms:
Much of the physical descriptions in the property forms were based on observations taken from the sidewalk. Did you see any errors in the description of your property?